## Slide 1: Weekly Progress Report
Yida Zhang
2023.8.7

## Slide 2
Complex Analysis and Integral Transformations: Two Chapters
Advanced Digital Signal Processing and Noise Reduction: One Chapter
Noise Reduction, Signal Reconstruction and Feature Selection on SCG Signal
Two paper:
Signal Processing Techniques for Removing Noise from ECG Signals
Novel Signal Noise Reduction Method through Cluster Analysis, Applied to Photoplethysmography
Progress

## Slide 3
Gaussian Process’s probability distribution
mean = 0
std = 1
mean = [0, 0]
cov = [[1, 0.5], [0.5, 1]]

## Slide 4
Pseudo-Random Number Generators (PRNG)
Mechanism of PRNG:
(1) Input an initial N-digit seed
(3) The N middle digits of the output is a random number
(2) Squares the seed to yield a 2N-digit output
(4) Treat the random number as a seed and go back to Step 1

## Slide 5
Huffman Coding
Input: 111233
Probability: 1: 3/6 2: 1/6 3: 2/6
Prob:1/2
(1)
Prob:1/6
(2)
Prob:1/3
(3)
Prob:1/2
(1)
Prob:1/6
(2)
Prob:1/3
(3)
Prob:1/2
Prob:1/2
(1)
Prob:1/6
Prob:1/3
Prob:1/2
Prob:1
1
1
0
0
0
(2)
(3)
10
11
Output:000101111

## Slide 6
Verification

## Slide 7
Respiration Signal Removal
Noise Reduction
Feature Extraction
Feature Selection

## Slide 8
Respiration Signal Removal
Pure SCG
Daubechies wavelet
Respiration Signal
seg_amp*np.sin(2*np.pi*seg_fre*x_space)
SCG with Respiration
SCG = Pure_SCG*(Respiration+2*seg_amp)

## Slide 9
Respiration Signal Removal
Assumption 1: The peaks of both peak1 and peak2 are fixed
Assumption 2: The respiration signal is a sinusoidal-shaped signal
Assumption 3: The respiration signal is added to the clean signal through multiplication
For peak1:
H = (P1 * Sin(wx) + 2 * P1) * P1
For peak2:
H = (P2 * Sin(wx) + 2 * P1) * P2
Known: H, x
Unknown: P1, P2, w
Method: Gradient Descent
  Input: x
  Output: H

## Slide 10
Respiration Signal Removal
Before Respiration Removal
train_set[244,:1000]
After Respiration Removal

## Slide 11
Noise Reduction
Reference: Novel Signal Noise Reduction Method through Cluster Analysis, Applied to Photoplethysmography
SCG without Respiration
Cluster 1: 8 signals
Cluster 2: 2 signals

## Slide 12
Signal Reconstruction
Average of Cluster 1
Signal with Noise
Reconstructed Signal

## Slide 13
Feature Extraction
# Mean
# P1 (Amplitude of Peak)
# P2
# P1-P2
# P1/P2
# D12 (Distance between P1 and P2)
# D21
# D11
# D12/D21
# Skew1
# Skew2
# Kurt1
# Kurt2
# Variance
# PeakToPeak
# Zero Crossing Rate
# Energy
# Number of Periods in 10 Seconds

## Slide 14
Feature Selection
Pearson correlation coefficient
Selected Features: D12, D12/D21, Skew1, Skew2, Kurt1, Kurt2

## Slide 15
Result (Without Feature Selection)
MAE: 6.04

## Slide 16
Result (With Feature Selection)
MAE: 6.9

## Slide 17
Possible Reasons
In our data, using the Pearson coefficient for feature selection is not suitable because we know that the peak value is also an important feature, but it has been filtered out. Maybe other methods of feature selection can get better result.
Feature selection is only effective when choosing a small number of features from many features such as select 10 from 1000. For a reduction from 12 features to 6 feastures, the effect is not significant.

## Slide 18
Study schedule (Next week)
Finish reading the remaining two papers and attempt to implement their methods
Complete the course on Complex Analysis
Choose an appropriate method for feature selection
Continue studying ADSPNR

## Slide 19
Question
Why the feature selection have a negtive effect on the result?

## Slide 20
Thanks for listening

## Slide 21
Verification